Hydrol. Earth Syst. Sci., 15, 3093–3100, 2011

www.hydrol-earth-syst-sci.net/15/3093/2011/

doi:10.5194/hess-15-3093-2011

© Author(s) 2011. CC Attribution 3.0 License.

Hydrology and Earth System Sciences

Technical  Note: Assessing a 24/7 solution for monitoring water

quality  loads in small river catchments

P. Jordan1,3 and R. Cassidy2

1 School of Environmental Sciences, University of Ulster, Coleraine, Northern Ireland, UK

2 School of Planning, Architecture and Civil Engineering, Queen’s University, Belfast, Northern Ireland, UK

3 Agricultural Catchments Programme, Teagasc, Johnstown Castle, Wexford, Republic of Ireland

Received: 13 May 2011 – Published in Hydrol. Earth Syst. Sci. Discuss.: 20 May 2011

Revised: 31 August 2011 – Accepted: 4 October 2011 – Published: 11 October 2011

Abstract.  Quantifying nutrient and sediment loads in catch-

ments is difficult owing to diffuse controls related to storm hydrology.  Coarse sampling and interpolation methods are prone to very high uncertainties due to under-representation of high discharge, short duration events.  Additionally, im- portant low-flow processes such as diurnal signals linked to point source impacts are missed. Here we demonstrate a so- lution based on a time-integrated approach to sampling with a standard 24 bottle autosampler configured to take a sam- ple every 7 h over a week according to a Plynlimon design. This is evaluated with a number of other sampling strategies using a two-year dataset of sub-hourly discharge and phos- phorus concentration data. The 24/7 solution is shown to be among the least uncertain in estimating load (inter-quartile range: 96 % to 110 % of actual load in year 1 and 97 % to

104 % in year 2) due to the increased frequency raising the probability of sampling storm events and point source sig- nals.  The 24/7 solution would appear to be most parsimo- nious in terms of data coverage and certainty, process sig- nal representation, potential laboratory commitment, tech- nology requirements and the ability to be widely deployed in complex catchments.

1   Introduction

Quantifying river transfers of chemical parameters, espe-

cially those relating to suspended sediments and/or higher discharges, remains a challenge to research and regulatory bodies owing to dependencies on storm hydrology (Bowes et al., 2009; Wall et al., 2011).  Phosphorus (P) and sedi- ment, for example, tend to be removed from land in rapid diffuse transfer events, via surface and near-surface hydro- logical pathways (Heathwaite and Dils, 2000; Deasy et al.,

2009) and the magnitude and rate of change of transfer is particularly influenced by land use (urban and agricultural in- tensities) and landscape permeability (soil permeability, ge- ology and prevalence of hard surfaces).  Highest risk is of- ten when these factors coincide with critical source areas for diffuse transfer (Gburek et al., 2002).   Transfers of P are also observed in rivers during lower flows, due to munic- ipal and domestic waste water discharges that may exhibit a diurnal pattern linked to the timing of discharge cycles (Palmer-Felgate et al., 2010).

Regulatory monitoring of P is considered especially im- portant as this is generally considered to be the limiting nu- trient in freshwater systems. There are exceptions, but for the most part, considerable additional efforts have been placed in national policies in many countries to deal with P from mu- nicipal and domestic effluents and from diffuse agricultural sources (e.g. OJEC, 1991a, b; OJEC, 2000). This monitoring is often spatially rich in terms of river network coverage but temporally poor and, as storm driven diffuse P transfers from agricultural land tend to form very significant contributions

Correspondence to: P. Jordan

(p.jordan@ulster.ac.uk)

Published by Copernicus Publications on behalf of the European Geosciences Union.

3094

P. Jordan and R. Cassidy: Assessing a 24/7 solution for monitoring water quality loads

to annual loads in rivers (Greene et al., 2011), low frequency

monitoring may be insufficient to monitor these transfers. This has potentially serious implications as competent au- thorities are charged with implementing agricultural mitiga- tion measures within legislation and monitoring the benefits at catchment scale (Mainstone et al., 2008).  Expectations of change from these national programmes, which in many countries are based on descriptive means of (up to) monthly sampling in rivers, may then be unrealised due to sampling strategies which are inadequate to identify change associated with mitigation effects.

Johnes (2007) clearly demonstrates the uncertainties in trying to collate sparse data into annual metrics of P load by deconstructing daily sampling from large catchments in the UK into less frequent datasets and applying interpolation and extrapolation algorithms.  Moatar and Meybeck (2007) also quantified the ranges in uncertainty associated with sub- sampling daily records at up to monthly frequencies for a range of chemical and particulate contaminants, including P, in six large catchments in both France and the US (Moatar and Meybeck, 2007).

Several methods have been used to overcome issues of sparse data samples with automatic water sampling used to target storm events or composite sampling to include a flow weighted element to account for higher flows (Lennox et al.,

1997; Jordan et al., 2001). However, targeted storm and com- posite sampling tends to avoid interim periods where process and chemical-biological interactions may be greatest (Hilton et al., 2006). More recently, automated bankside spectropho- tometric equipment has been used to monitor P on a near continuous basis (Jordan et al., 2007; Palmer-Felgate et al.,

2010; Wall et al., 2011) but, while giving temporally rich data, these systems are never likely to be spatially rich owing to capital and maintenance costs.

There is, therefore, a requirement to add complimentary monitoring to national programmes that is sufficient to mon- itor all flow regimes in rivers.  Such monitoring should ac- count for the influences of point and diffuse P transfers, where these are likely, provide process information such as diurnal cycling and hysteresis patterns, respectively, and en- able trajectories of change for all transfer types to be audited. Recent work in the Plynlimon experimental catchment has used an alternative strategy based on the use of an automatic water sampler with a 24 bottle configuration set to sample on a 7 h basis (Neal et al., 2011;  Halliday et al., 2011). This “24/7” configuration can be used for total chemical species and conservative solutes if the sampler is retrieved

on a weekly basis.

In this paper, we evaluate the 24/7 sampling and other con- figurations, which are feasible using standard field autosam- pling equipment, by deconstructing and sampling a two-year sub-hourly time series of discharge and P chemistry. Loads are estimated for all sample sets and the aggregated results compared across all sampling configurations.

2   Methods

Data were used from a hydrometric and hydrochemical mon-

itoring station in Co. Monaghan, Ireland. The station set-up is described in detail elsewhere (Jordan et al., 2005, 2007; Cassidy and Jordan, 2011). In summary, discharge was mon- itored at a rated station at 5 km2  in a catchment draining grassland agriculture on drumlin soils. This landscape type is predisposed to high P transfers during storm events (Dou- glas et al., 2007) and high background P concentrations dur- ing low flows from scattered point sources (Arnscheidt et al., 2007).  These transfers were monitored by a Dr. Lange Sigmatax-Phosphax suite of instruments that samples river water and analyses TP on a 20 min time-step (3 samples each every hour).  Data were extracted over two hydrologi- cal years, quality controlled and assessed for completeness. During 2006–2007 and 2007–2008, discharge/TP data were

100 %/94 % and 100 %/98 % complete, respectively. Loads were calculated from discharge and TP concentration by in- terpolation of the 20 min time series (Eq. 3).

Sampling was simulated by applying a numerical algo- rithm to generate all possible sample sets from the sub-hourly time series, based on a set of caveats for each sampling strat- egy, and combining both systematic and Monte-Carlo ap- proaches. For the 24 weekly samples a random and 7 h inter- val were assessed:

1. 24 samples at 7 h intervals

- Sampling to be initiated between 8 a.m. and 6 p.m., and restricted to Monday to Friday to correspond to normal working hours during which an autosampler would be deployed and initiated.

2. 24 samples at random times over 7 days

- The autosampler would be programmed to take sam- ples at 24 random times during the week, with each set of time stamps generated weekly and uploaded to the autosampler.

For comparison, sample sets were also generated for monthly, weekly, daily and random sampling frequencies as described in Cassidy and Jordan (2011) and also at sub-daily frequencies less than and greater than the 7 h sampling fre- quency (Table 1).

Loads were estimated for each sample set using a standard flux-based approach (Method 5 in Littlewood et al., 1998), also known as the first-choice Paris Commission algorithm (PARCOM, 1992), to estimate load LE (kg) as:

K  n

(CiQ i)

= 1

LE =

with

i

·Q r

(1)

n

1 Q i

i=

N

Q k

= 1

Q r = k

(2)

N

Hydrol. Earth Syst. Sci., 15, 3093–3100, 2011

www.hydrol-earth-syst-sci.net/15/3093/2011/

P. Jordan and R. Cassidy: Assessing a 24/7 solution for monitoring water quality loads

3095

Table 1. Series of sampling solutions used to estimate TP load based on the PARCOM algorithm (Eq. 1) showing the number of sample sets

and samples per set used in each estimate.

Number of

sample sets

Number of

samples per set

Sampling Strategy

1

2

3

4

5

6

7

8

9

10

11

12

13

14

15

16

Random 10 (10 random samples annually)

Monthly

Weekly (during normal working hours, 08:00–18:00) Weekly (any time- assumes pre-set autosampler) Weekly + sampling when Q < 10th Percentile1

Random 60 (60 random samples annually)

24 hourly samples on a day each week (autosampler) Random 360 (360 random samples annually)

Daily Sampling (08:00–18:00) Nightly Sampling (18:00–08:00)

12 h sampling intervals

24 samples per week – random intervals

24 samples per week – uniform intervals

24 samples per week + hourly samples when Q < 10th percentile

6 h sampling intervals

3 h sampling intervals

100

180

120

300

180

100

14

100

181

181

151

151

151

151

151

151

10

12

52

52

117

60

1248

360

365

365

730

1248

1248

1508

1428

2846

1 Autosampler triggered when stage height exceeds pre-set limit.

where Ci is the instantaneous TP concentration (mg l− 1 ), Q i is the instantaneous discharge (m3 s− 1 ), and Q r is the aver- age discharge, based on higher frequency discharge records over that sampling duration. K is a constant which accounts for the duration of the record. Q k is the recorded discharge at 20 min intervals.

The load was estimated for each sample set from each sampling strategy and aggregated for comparison with the “20 min interpolated load”, LT , based on the sub-hourly data, which was calculated as:

Random (10 samples) and monthly sample estimates were

highly inaccurate with 25th and 75th interquartile ranges well below the 20 min interpolated load calculations and only maximum estimates within the datasets being over-estimates and excessively so in 2006–2007.  Accounting for storm events through additional triggered sampling when Q < 10th percentile increased the median load and produced an im- provement on the standard weekly strategies, with greatest effect in 2006–2007. Random sampling (360 samples) per- formed well by comparison with other lower frequency ap- proaches (median = 97.2 % in 2006–2007; median = 104.8 % in 2007–2008). This is attributed to the clustering inherent in randomly distributed points (sample times) providing a good likelihood of investigating the full spectrum of TP variability in the annual data set without bias, while the sample num- ber (the average frequency is approximately equivalent to daily sampling) increases the probability of sampling a broad range of event sizes.

Daily sampling, while resulting in a smaller range of esti- mated loads compared with the lower frequency approaches, still underestimated load with the interquartile range (IQR) for  both  years ranging between 72  and  88 %  of  the  20 min interpolated load for 2006–2007 and 91 to 95 % for

2007–2008.  This strategy was based on operational con- siderations where samples could only be collected during a working day between 08:00 and 18:00.  However, when this strategy was changed to sample during overnight pe- riods (18:00 to 08:00), the resulting sample sets tended to over-estimate annual load due to higher TP concentrations as observed with the 20 min data during non-storm periods

tend

LT =	Q(t)C(t)dt

tstart

where, over a sampling period (tstart to tend ), Q

(3)

is the instan-

taneous discharge and C the instantaneous concentration at sample time t.

3   Results and discussion

The several hundred datasets generated by simulation and ap-

plied to the flux-based load algorithm (Eq. 1) were plotted as loads in box whisker plots and compared with the 20 min in- terpolated load of high resolution data (Eq. 3) (Fig. 1a and b). The 20 min interpolated load was calculated as 1608 kg in

2006–2007 and 1880 kg in 2007–2008. In general, all sam- pling strategies gave variable estimates of TP load when used with the algorithm.  However, as might be anticipated, the distribution in this variation was greater with decreased ini- tial sample frequency and less so with increased frequency.

www.hydrol-earth-syst-sci.net/15/3093/2011/

Hydrol. Earth Syst. Sci., 15, 3093–3100, 2011

3096

P. Jordan and R. Cassidy: Assessing a 24/7 solution for monitoring water quality loads

Fig. 1. Box whisker plots showing development of estimated loads (25th, 50th, 75th percentiles, maximum and minimum) using systematic

and random sample sets from a decimated sub-hourly dataset of P concentration and discharge in 2006–2007 (a) and 2007–2008 (b).

(median = 114 %, IQR = 101–131 % of 20 min interpolated

load for 2006–2007; median = 107 %, IQR = 99–115 % for

2007–2008).   The diurnal variation in concentration, with an increase during evening and at night, is evident in the low flow time series shown in Fig. 2b and may be at- tributed both to a decline in biological activity at night lead- ing to reduced uptake of P and (more likely – Arnscheidt et al., 2007) an increase in household activity either side of the working day and hence a peak in point source pres- sures.   A compromise was shown to be a 12 h sampling

regime that was able to capture both day and night time sam-

ples (median = 103 %, IQR = 97–112 % of 20 min interpo- lated load for 2006–2007; median = 102 %, IQR = 97–105 % for 2007–2008).

Good estimates to the 20 min interpolated load were also generated by the 24 samples (at 7 h intervals) per 7 days (24/7)  approach (median = 106.2 %,  IQR = 96.6–110 %  of

20 min interpolated load for 2006–2007; median = 101.4 %, IQR = 97.3–104.3 %  for  2007–2008).    The  random sam- pling  24/7  approach  gave  a  similar  result,  though  with

Hydrol. Earth Syst. Sci., 15, 3093–3100, 2011

www.hydrol-earth-syst-sci.net/15/3093/2011/

P. Jordan and R. Cassidy: Assessing a 24/7 solution for monitoring water quality loads

3097

Fig. 2. Representation of a period of discharge and diffuse P transfer during a diffuse storm event (a) with sub-hourly data (solid line), 7

hourly sampling (open circles) and daily sampling (closed triangles). Seven hourly sampling is more likely to capture important times of hydrograph and chemograph development. Also, (b) important diurnal signals during point source P transfers are better represented using the 7 hourly sampling and are missed with daily sampling which, by coinciding with a daily peak in the cycle, may overestimate mean daily low flow concentrations (and similarly underestimate if sampled 12 h previously).

a larger range (median = 100.1 %,  IQR = 94.2–107.5 % of

20 min interpolated load for 2006–2007; median = 99.5 %, IQR = 92.4–105.4 %  for  2007–2008).    Similarly,  sample sets  for  sampling  intervals  less  than  7 h  generated  esti- mates of annual load that were close to the 20 min inter- polated load and with low variability (e.g. 6 h interval: me- dian = 104.4 %, IQR = 103.1–106.2 % of 20 min interpolated load for 2006–2007; median = 99.5 %, IQR = 95.6–104.8 % for 2007–2008: 3 h interval: median = 104.5 %, IQR = 103.2–

105.4 % of 20 min interpolated load for 2006–2007; me- dian = 100.3 %, IQR = 99.6–100.9 % for 2007–2008). How- ever, increasing the sample frequency from 7 h to include samples when Q < 10th percentile flow biased the loads to over-estimate compared with the 20 min interpolated load (median = 132.0 %, IQR = 130.4–136.2 % of 20 min interpo-

lated load for 2006–2007; median = 121.2 %, IQR = 120.4–

122.6 % for 2007–2008).

The improved load estimates using the sub-daily ap- proaches are directly attributable to the increased probability of capturing short term fluctuations in concentration. Storm events and diffuse P transfers are often of hours rather than days duration and have a much increased sampling probabil- ity at lower intervals (Fig. 2a). The close agreement between

12 h and 24/7 estimated loads indicates that these regimes may be desirable in terms of parsimony of cost, effort and data coverage. The 24/7 approach, for one extra sample per day compared with the 12 h regime, also has the advantage of sampling each hour of the day during a 7 day period (Hall- iday et al., 2011) for more representative coverage. Apparent also in the 24/7 sub-sample datasets were the representation

www.hydrol-earth-syst-sci.net/15/3093/2011/

Hydrol. Earth Syst. Sci., 15, 3093–3100, 2011

3098

P. Jordan and R. Cassidy: Assessing a 24/7 solution for monitoring water quality loads

of non-storm discharge periods with important diurnal pro-

cesses represented possibly relating to point P transfers, as noted above, that were absent in the daily sampling (Fig. 2b). Inherent with sampling at the same time daily is the risk of coinciding with diurnal discharges from agricultural or wastewater treatment works and, therefore, either under or overestimating the low flow concentration by coinciding with either a peak or trough in the cycle.

The scale of the river catchment and landscape type used in this study (flashy hydrology with a low baseflow index, high magnitude diffuse P transfers and high frequency point source signals) is typically a challenge for most sampling strategies not based on near continuous data collection. Most of the total annual load can result from higher concentra- tion, short duration events for which sampling probabilities decrease as a power-law with increasing concentration (see Cassidy and Jordan, 2011 for a discussion).  Sampling as much of the concentration range as possible is desirable and the improved coverage provided by 24/7 sampling, compared with daily sampling, is demonstrated by examining the pro- portion coverage of the concentration range by the sample sets for each strategy (Fig. 3).  It is a scale, however, that is useful in monitoring the influences of changed policy ex- pediencies towards catchment management such as the Ni- trates Directive and other programmes of measures linked to the EU Water Framework Directive (Wall et al., 2011). This landscape type is again a useful benchmark to demonstrate that TP patterns linked specifically to source, viz. point, dif- fuse and incidental (Jordan et al., 2007) and where these pat- terns, independent of annual load, change according to spe- cific mitigation measures.

The attractiveness of using the 24/7 approach, for conser- vative analytes at least, is that it can be achieved using low- technology and off-the-shelf autosampling equipment at ex- isting hydrometric stations, and the pump-type samplers with a 24-bottle configuration are ubiquitous items of monitoring equipment. Personnel requirements and laboratory resources are also easily timetabled on a once per week basis (C. Neal, personal communication, 2011) and if TP load is preferred over pattern then the 24 samples can be composited in the laboratory according to flow-weighted volumes using weekly hydrometric data.

There are, however, some issues related to extreme events and non-conservative analytes. The 24/7 approach only gives scope for 3 samples every 24 h and this, in some very small catchments, may not be enough to sample extreme storm events that can dominate the annual transfers of P and sed- iment.  It is here, even for less extreme events, that uncer- tainty in the box whisker plots in Fig. 1 is generated during the higher flow events.  Again, this may not be so much of an issue as scale and catchment buffering increases at larger national monitoring sites.  The non-conservative nature of some analytes is, however, not so readily accommodated. Depending on what the objectives of the monitoring are will be important as, for example, chemical-ecological relation-

Fig. 3.  Percentage coverage of the TP concentration range by the

sample sets using the 24/7 sampling solution (closed symbols) and daily sampling solution (open symbols).  The 24/7 solution is ap- proximately twice as likely to sample higher TP concentrations,

with for example, 100 % of the 24/7 sample sets containing sam- ples in the 1 mg l− 1 range while only 50 % of the daily sample sets contain values in the same range.

ships are more likely to be linked to soluble nutrient status of

water bodies. Total reactive P and other soluble P fractions may not be amenable to being left in sample bottles for up to

7 days (Haygarth et al., 1995) and possibly the best that can be achieved is for samples taken from the last three bottles for immediate processing on return to the laboratory. Other conservative solutes and sediments are easily accommodated (Neal et al., 2011).

In other, larger catchments, where hydrological buffer- ing due to scale, soil type and geology may decrease runoff flashiness and possibly where there is a stronger diffuse pol- lution signal (or this is the most important signal to mon- itor in very small catchments), it may not be necessary to increase sample resolution during non-storm periods. Here, other workers have shown that the variation in non-storm transfers is small enough for the emphasis to be on storm events (e.g. Kronvang and Bruhn, 1996). Additionally, vari- ability in flux for a range of chemical and particulate contam- inants (in catchments > 1000 km2 )may be predictable based on the percentage of long-term flux transported in a small percent of the time (Moatar and Meybeck, 2007). However, in many catchments, there is an increasing recognition of the interaction between nutrient sources related to flow regime (e.g. Hilton et al., 2006).  For example, in river base flows Cassidy and Jordan (2011), indicate that data from monthly sampling are likely to be useful in capturing low flow signals from the high probability of sampling these high frequency flows (and their point source impacts – if present) and this

Hydrol. Earth Syst. Sci., 15, 3093–3100, 2011

www.hydrol-earth-syst-sci.net/15/3093/2011/

P. Jordan and R. Cassidy: Assessing a 24/7 solution for monitoring water quality loads

3099

is also indicated by Foy (2007) in large river systems. This

creates a conundrum for agencies that are required to monitor the benefits accruing from both diffuse and point source miti- gation measures and especially relationships with ecological metrics in flowing and standing waters and it may be that a moderate to high degree of empiricism is required before looking to reduce to a coarser sampling regime. In the anal- ysis in the current study, the different resolution sampling regimes have at least been tested with a much higher resolu- tion dataset to resolve these important signals and which is likely to provide a richer dataset at larger scales – this could then be subsequently tested for further parsimony if required.

Acknowledgements. We  acknowledge  the  contribution  to  data

collection by Joerg Arnscheidt, Hugo McGrogan and Pete Devlin, School of Environmental Sciences, University of Ulster.  We also thank Colin Neal, CEH Wallingford, for recent discussions and enthusiasm regarding high resolution chemistry data collection in rivers.

Edited by: L. Pfister

References

Arnscheidt, J., Jordan, P., Li, S., McCormick, S., McFaul, R., Mc-

Grogan, H. J., Neal, M., and Sims, J. T.: Defining the sources of low-flow phosphorus transfers in complex catchments, Sci. Total Environ., 382, 1–13, 2007.

Bowes, M. J., Smith, J. T., and Neal, N.:  The value of high- resolution nutrient monitoring: A case study of the River Frome, Dorset, UK, J. Hydrol., 378, 82–96, 2009.

Cassidy, R. and Jordan, P.: Limitations of instantaneous water qual- ity sampling in surface-water catchments: comparison with near- continuous phosphorus time-series data, J. Hydrol., 405, 182–

193, 2011.

Deasy, C., Brazier, R. E., Heathwaite, A. L., and Hodgkinson, R.: Pathways of runoff and sediment transfer in small agricultural catchments, Hydrol. Process., 23, 1349–1358, 2009.

Douglas, R. W., Menary, W., and Jordan, P.: Phosphorus and sedi- ment transfers in a grassland river catchment, Nutr. Cycl. Agroe- cosyst., 77, 199–212, 2007.

Foy, R. H.: Variation in the reactive phosphorus concentrations in rivers of northwest Europe with respect to their potential to cause eutrophication, Soil Use Manage., 23, 195–204, 2007

Gburek, W. J., Drungil, C. C., Srinivasan, M. S., Needelman, B. A., and Woodward, D. E.:  Variable-source-area controls on phos- phorus transport: Bridging the gap between research and design, J. Soil Water Conserv., 57, 534–543, 2002.

Greene, S., Taylor, D., McElarney, Y., Foy, R. H., and Jordan, P.: An evaluation of catchment-scale phosphorus mitigation using load apportionment modelling, Sci. Total Environ., 409, 2211–2222,

2011.

Halliday, S. J., Wade, A. J. Skeffington, R. A. Neal, C. Reynolds, B. Rowland, A. P., Neal, M. and Norris, D.: An analysis of long- term trends, seasonality and short-term dynamics in water quality data from Plynlimon, Wales, Sci. Total Environ., in press, 2011. Haygarth, P. M., Ashby, C. D. and Jarvis, S. C.: Short term changes in the molybdate reactive phosphorus of stored soil waters, J.

Environ. Qual., 24, 1133–1140, 1995.

Heathwaite, A. L. and Dils, R. M.: Characterising phosphorus loss in surface and subsurface hydrological pathways, Sci. Total Env- iron., 251–252, 523–528, 2000.

Hilton, J., O’Hare, M., Bowes, M. J., and Jones, J. I.: How green is my river: A new paradigm in eutrophication in rivers, Sci. Total Environ., 365, 66–83, 2006.

Johnes, P. J.: Uncertainties in annual riverine phosphorus load es- timation: Impact of load estimation methodology, sampling fre- quency, baseflow index and catchment population density, J. Hy- drol., 332, 241–258, 2007.

Jordan, P., Rippey, B., and Anderson, N. J.: Modeling Diffuse Phos- phorus Loads from Land to Freshwater Using the Sedimentary Record, Envir. Sci. Tech., 35, 15–819, 2001.

4   Conclusions

A two year, sub-hourly data-set of synchronous discharge and P concentration from a flashy 5 km2 catchment was de-

constructed into artificial data-sets of coarser resolution, and a numerical algorithm was used to generate sample sets both systematically and with a Monte-Carlo approach.  Sample sets were collated into annual P loads using a standard flux- based algorithm based on metrics of instantaneous discharge and concentration with findings that:

– In this catchment, with examples of point and diffuse P transfer, daily sampling tended to underestimate load with an IQR between 72 and 88 % of the 20 min interpo- lated load and failed to reveal important sub-daily trans- port patterns.

– A 24/7 sampling solution based on a Plynlimon de- sign and modelled on an auto-sampler generating 24 samples per  week on  a  7 h  cycle improved the  es- timated load variability (IQR = 96.6–110 % for 2006–

2007; IQR = 97.3–104.3 % for 2007–2008) and also re- vealed sub-daily patterns related to point and diffuse P transfers which can be used to monitor trajectories of change from both signals.

– Sub-7 h samples showed small reductions in load esti- mate variability but the 24/7 design is more easily im- plemented and is likely to improve the coverage of all metrics (annual load, sub-daily patterns, etc) as catch- ment scale increases; with, for example, hydrological buffering increasing to higher baseflow indices (due to soil and geology influences on runoff) and the interac- tion of multiple P sources diminishing.

– Implemented as a complimentary part of forward na- tional WFD monitoring, the 24/7 solution is likely to be a parsimonious and cost effective compromise between spatially rich routine monthly sampling and temporally rich fully automated bankside analysis and could form the basis of further reductions in sample resolution when used as a comparative dataset at larger scales.

www.hydrol-earth-syst-sci.net/15/3093/2011/

Hydrol. Earth Syst. Sci., 15, 3093–3100, 2011

3100

P. Jordan and R. Cassidy: Assessing a 24/7 solution for monitoring water quality loads

Jordan, P.,  Arnscheidt, J.,  McGrogan, H., and McCormick, S.:

High-resolution phosphorus transfers at the catchment scale: the hidden importance of non-storm transfers, Hydrol. Earth Syst. Sci., 9, 685–691, doi:10.5194/hess-9-685-2005, 2005.

Jordan, P., Arnscheidt, A., McGrogan, H., and McCormick, S.: Characterising phosphorus transfers in rural catchments using a continuous bank-side analyser, Hydrol. Earth Syst. Sci., 11, 372–

381, doi:10.5194/hess-11-372-2007, 2007.

Kronvang, B. and Bruhn, A. J.: Choice of sampling strategy and es- timation method for calculating nitrogen and phosphorus trans- port in small lowland streams, Hydrol. Process., 10, 1483–1501,

1996.

Lennox, S. D., Foy, R. H., Smith, R. V., and Jordan, C.: Estimating the contribution from agriculture to the phosphorus load in sur- face water, in: Phosphorus Loss from Soil to Water, edited by: Tunney, H., Carton, O. T., Brookes, P. C., and Johnstown, A. E., CAB, Wallingford, 55–75, 1997.

Littlewood, I. G., Watts, C. D., and Custance, J. M.: Systematic ap- plication of United Kingdom river flow and quality databases for estimating annual river mass loads, Sci. Total Environ., 210/211,

21–40, 1998.

Mainstone, C. P., Dils, R. M., and Withers, P. J. A.: Controlling sed- iment and phosphorus transfer to receiving waters – A strategic management perspective for England and Wales, J. Hydrol., 350,

131–143, 2008.

Moatar, F. and Meybeck, M.:  Riverine fluxes of pollutants:  To- wards predictions of uncertainties by flux duration indicators, C. R. Geosci., 339, 367–382, 2007.

Neal, C., Reynolds, B., Rowland, P., Norris, D., Kirchner, J.W.,

Neal, M., Sleep, D., Lawlor, A., Woods, C., Thacker, S., Guyatt, H., Vincent, C., Hockenhull, K., Wickham, H., Harman, S. and Armstrong, L.: High-frequency water quality time series in pre- cipitation and streamflow: from fragmentary signals to scientific challenge, Sci. Total Environ., in press, 2011.

Official Journal of the European Community:  Council Directive

91/676/EEC of 12 December 1991 concerning the protection of waters against pollution caused by nitrates from agricultural sources, 1991a.

Official Journal of the European Community:  91/271/EEC of 21

May 1991 concerning urban waster-water treatment, 1991b. Official Journal of the European Community: Establishing a frame-

work for community action in the field of water policy (Water

Framework Directive), 2000/60/EC (2000), 2000.

Palmer-Felgate, E. J., Mortimer, R. J. G., Krom, M. D., and Jarvie, H. P.: Impact of point-source pollution on phosphorus and nitro- gen cycling in stream-bed sediments, Environ. Sci. Technol., 44,

908–914, 2010.

PARCOM: Principles of the Comprehensive Study on Riverine In- puts. Tenth Meeting of the Paris Commission. London, 1992.

Wall, D., Jordan, P., Melland, A. R., Mellander, P.-E., Buckley, C., Reaney, S. M., and Shortle, G.: Using the nutrient transfer con- tinuum concept to evaluate the European Union Nitrates Direc- tive National Action Programme, Environ. Sci. Policy, 14, 664–

674, 2011.

Hydrol. Earth Syst. Sci., 15, 3093–3100, 2011

www.hydrol-earth-syst-sci.net/15/3093/2011/